CSE 3302 Notes 9:  Data Abstraction

(Last updated 11/17/15 1:53 PM)

References:  Gabbrielli:  9

9.1.  Abstract Data Types

Programmer-defined types should be handled like built-in types

Primary characteristics:

1.	Type name

2.	Underlying representation (concrete type)

3.	Set of operation names

4.	Implementation for each operation

(pop returns a reference to the modified stack,  top returns last-in without mutating)

5.	Opaque interface separating 1. and 3. from 2. and 4.

Stack of integers example:

1.	Figure 9.1, no opaque interface

2.	Figure 9.2, adds 5. in form of signature

9.2.  Information Hiding

Based on opaque interface the principle of representation independence (p. 271) holds:

Two correct implementations of (a single specification) of an ADT  are operationally indistinguishable by the clients of the types.

Constructor, transformers/operators (Liskov/Wing call these mutators), observers

9.3.  Modules

Module:  One or more ADTs encapsulated together

Import:  Accessing a module for purposes of instantiating

Figures 9.5 and 9.6 (p. 273-274)

9.3.  Some Items from W.R. Cook Paper

Figures 2 and 3, integer sets as ML ADT for specification only

Figure 4, integer set using sorted lists as representation

Disadvantage of many ADT mechanisms:  only one implementation per ADT name

Notable Exceptions:

C header files and separately compiled implementations (e.g. makefiles as glue)

C++ (pointer to implementation) pimpl idiom - to avoid recompilation

https://en.wikipedia.org/wiki/Opaque_pointer

Java interfaces and generics

C++ templates

Sections 2.4 and 2.5

Existential type = ADT name and operations (Figure 6), but where implementations may differ

Using different implementations for one ADT gives different incompatible types, e.g. mixing

two recursive implementations

Transition to Notes 10:

From P. Wegner, “Dimensions of object-based language design”, OOPSLA ’87 http://dl.acm.org.ezproxy.uta.edu/citation.cfm?doid=38765.38823